## Slide 1: hwdbg Debugging Hardware Like Software
Sina Karvandi
Spring 2024

## Slide 2: “To err is human, to debug is divine.”

## Slide 3
hwdbg is a new debugger chip generator based on chisel language (scala) & LLVM circt
hwdbg.hyperdbg.org/docs

## Slide 4: Outline
01 Introduction
02 Design
03 Sensors
04 Scripting Language
05 D.F.R.
06 Evaluation
Questions

## Slide 5: Outline
01 Introduction
  What is HyperDbg?
  Main Motivation
  Key Contributions
  Software, Hardware Platform
  Key Features
  Debugging Modes
02 Design
03 Sensors
04 Scripting Language
05 D.F.R.
06 Evaluation
Questions

## Slide 6: Introduction 01
The motivation behind creating a new debugger

## Slide 7: What is HyperDbg?
HyperDbg is an open-source platform that brings debugging infrastructures like hypervisor-assisted, user-mode, and kernel-mode debuggers mainly with a focus on using modern hardware technologies for analyzing, fuzzing, and reversing.

## Slide 8: Main Motivation
The key intuition behind hwdbg is making security researchers and hardware engineers able to run custom action in the smallest (shortest) event in a digital circuit which is the changes (rising-edge & falling-edge) within the clock cycle.

## Slide 9: Key Contributions
hwdbg comes with these contributions.
Introduction of a Unified Debugging Framework
Open-source and Customizable Tool
Integration with FPGAs
Robust Debugging Experience
Enhancement of Reverse Engineering and Chip Fuzzing Capabilities
Comprehensive Scripting Support

## Slide 10: 01 Hardware Platform Software 02 03
The hardware side will be written in chisel programming language as well as Verilog and SystemVerilog.
The testing platform is AMD Xilinx FPGAs.
The software side is implemented in C/C++ for sending debugging commands and parsing scripts.

## Slide 11: Key Features Signal Analyzer Signal Manipulator Testing & Fuzzing Software Abstractions
An open-source logic analyzer
Manipulating digital signals by changing the state of wires
Automatic testing and fuzzing of chips by software generated testcases
Simulate software debugging concepts in hardware

## Slide 12: Debugging Modes Passive debugging Active debugging
In this debugging mode, hwdbg acts as an introspection tool, and monitors different signals to the target debugging module.
In this debugging mode, hwdbg is able to both monitor and manipulate signals (Input/Output). These signal modifications are configured by the user’s custom scripts.

## Slide 13: Outline
01 Introduction
02 Design
  PS <> PL Communication
  Communication Modules
  Input/Output Ports
  BRAM Simulator
  BRAM Simulator Waves
03 Sensors
04 Scripting Language
05 D.F.R.
06 Evaluation
Questions

## Slide 14: Design 02
The proposed debugger chip generator design

## Slide 15: PS <> PL Communication
hwdbg communicates from PS to PL by using a shared BlockRAM over the AXI bus, as well as an interrupt line from PL to PS and a shared GPIO line from PS to PL.

## Slide 16: Communication Modules —Sending Module —Send/Receive Synchronization Module —Receiving Module —Interpreting Module
Sending module is responsible for preparing mandatory headers and write to BRAM as well as interrupting PS.
Because only one BRAM port is shared with PL, synchronization is needed to avoid data corruption in case of simultaneous writes.
Once share PS <> PL line is high, receiving verifies BRAM data headers and notifies interpreter.
Once a valid packet is received, the interpreting module configures the chips and sends the response to the debugger.

## Slide 17: Input/Output Ports
This picture illustrates the input/output pins of the hwdbg design.

## Slide 18: BRAM Simulator
Here is the BRAM simulator (PS to PL area).

## Slide 19: BRAM Simulator (cont.)
Here is the BRAM simulator (PL to PS area).

## Slide 20: BRAM Simulator Waves
Here is the BRAM simulator wave results for hwdbg.

## Slide 21: Outline
01 Introduction
02 Design
03 Sensors
  Side-channel Attacks in Microchips/IP Cores
  Physical Unclonable Function (PUF)
  Debugging Sensors
04 Scripting Language
05 D.F.R.
06 Evaluation
Questions

## Slide 22: Sensors 03
The debugging sensor modules embedded in the hwdbg debugger

## Slide 23: Side-channel Attacks in Microchips/IP Cores
A side-channel attack in chips and IP cores involves exploiting indirect information leakage, such as power consumption or electromagnetic emissions, to extract sensitive data.
We use sensors like Ring Oscillators (RO) for detecting these side channels because they can monitor variations in hardware characteristics, which may indicate the presence of side-channel leakage or attacks.

## Slide 24: PUF
Physical Unclonable Function
A PUF is a physical entity utilized in microchips and other electronic devices to generate unique, device-specific cryptographic keys based on the uncontrollable physical variations that occur during the manufacturing process.
These unique differences, such as variations in silicon pathways, ensure that each PUF is unique and make it theoretically impossible to duplicate or clone.

## Slide 25: Debugging Sensors IDELAYE2/3 Time-to-Digital Converter (TDC) Ring Oscillator (RO)
Provides adjustable signal delay capabilities for timing adjustments and alignment in high-speed circuits.
Converts the time interval between two events into a digital value for precise timing measurements.
Measures variations in signal propagation delay to detect changes in environmental conditions or circuit behavior.

## Slide 26: Debugging Sensors (cont.) Frequency & Clock Sensors Temperature Sensor Voltage Sensor
Monitors the frequency and stability of clock signals to ensure they remain within the expected range and performance criteria.
Measures the temperature within the chip to monitor thermal conditions and prevent overheating.
Monitors and measures the voltage levels within a circuit to ensure stable and correct operation.

## Slide 27: Outline
01 Introduction
02 Design
03 Sensors
04 Scripting Language
  Script Execution Stages
  Ports & Pins
  Supported Statements
  Supported Operators
  Example Script 1
  Example Script 2
05 D.F.R.
06 Evaluation
Questions

## Slide 28: Scripting Language 04
HyperDbg’s dslang variation for hardware debugging

## Slide 29
Script Execution Stages
This picture demonstrates the execution of different IR scripts in each stage.

## Slide 30: Ports & Pins
Registers | Pseudo-registers
@hw_pin0 | $hw_clk, or $hw_clock: 1 or 0
@hw_pin1 | $hw_counter and, $hw_clock_edge_counter
@hw_pinX | $hw_clock_frequency
@hw_port0 | $hw_stage: Stage number of script
@hw_port1 | 
@hw_portX | 

## Slide 31: Supported Statements
Functions
Memory Modification
Register and Variable Assignment
External Argument
Conditional Statements
Arguments as $arg0, $arg1, etc.
if, else, elsif statements
Changing pins and ports (registers) and assign to variables
Modifying the BRAM memory
Defining custom function

## Slide 32: Supported Operators
Precedence | Operators
Parentheses | ( )
Unary Operators | -, +, ~, &, *
Arithmetic Operators | *, /, %
Arithmetic Operators | +, -
Shift Operators | >>, <<
Comparison Operators | >=, <=, >, ==, !=
Bitwise AND Operator | &
Bitwise XOR Operator | ^
Logical AND Operator | &&
Logical OR Operator | ¦¦

## Slide 33: Example Script 1
? {
if (@hw_port5 == 55) {
printf(“@hw_port5 is equal to 0x55\n");
}
elsif(@hw_port5 == 66) {
printf(“@hw_port5 is equal to 0x66\n");
}
elsif(@hw_port5 == 77) {
printf(“@hw_port5 is equal to 0x77\n");
} else {
printf(“@hw_port5 is not equal to 0x55, 0x66, 0x77. It is equal to %llx\n", @hw_port5);
}
}

## Slide 34: Example Script 2
? {
int my_func1(int var1) {
result = var1 + 1;
printf("my_func1 %d\n", result);
return result;
}
int my_func2(int var1) {
result = var1 * 2;
printf("my_func2 %d\n", result);
return result;
}
int my_func3(int var1) {
result = my_func1(var1) + my_func2(var1);
printf("my_func3 %d\n", result);
return result;
}
printf("%d\n", my_func3(2));
}

## Slide 35: Outline
01 Introduction
02 Design
03 Sensors
04 Scripting Language
05 D.F.R.
  Key (must-have) Software Debugger Features
  Debugging Hardware Like Software
  Software Stepping in Hardware
  Anomaly Definition
  Fuzzing & Fault-Injection
06 Evaluation
Questions

## Slide 36: D.F.R. 05
Debugging, Fuzzing, Reversing

## Slide 37: Key (must-have) Software Debugger Features
Reading/Writing Memory
Inspecting/Modifying Registers Values
Stepping Through Instructions
Putting Breakpoints and Pausing The Debuggee

## Slide 38: Debugging Hardware Like Software Logic Analyzer Emulation of Instruction Stepping by Controlling Clock Signal Signal Inspection and Modification Cutting The Signals Based on Conditions
Reading/Writing Memory
Stepping Through Instructions
Inspecting/Modifying Registers Values
Putting Breakpoints and Pausing The Debuggee

## Slide 39: Software Stepping in Hardware
Once we can control the clock signal, we are able to see and modify I/O ports at each cycle.
The next rising-edge clock will be inserted once the introspection/modification is done.
Not possible in chips with internal clock sources.

## Slide 40: Anomaly Definition Anomalies In Expected Functionalities Anomalies Based On Sensors Indications
These occur when the device fails to compute the correct output due to specific inputs, detectable through emulation.
Sensors can indicate anomalies through abnormal state changes, signaling potential internal issues in the chip.

## Slide 41: Fuzzing & Fault-Injection Cut Singal Fuzzing Change Clock domain
Remove signal at different random stages
Providing random software generated data and observe the output
Using PWM with different duty cycles

## Slide 42: Outline
01 Introduction
02 Design
03 Sensors
04 Scripting Language
05 D.F.R.
06 Evaluation
  dslang vs. TSM
  Source code
Questions

## Slide 43: Evaluation 06
Evaluating hwdbg debugger chip generator

## Slide 44: dslang vs TSM
 | hwdbg (dslang) | Xilinx ILA (TSM)
Can act as a logic analyzer | Yes | Yes
Speed comparison | Slower | Faster
Can trigger an event (e.g., a breakpoint) | Yes | Yes
Has debugging sensors | Yes | No
Can modify signals on the fly (configurable) | Yes | No
Can interpret complex computations | Yes | No
Supports on-the-fly configuration | Yes | No
Notify the debugger without triggering event | Yes | No
Supports software stepping | Yes | No
Simplicity of state machine scripting | Simpler, software-like scripting | More complex
Can perform stepping fault-injection and signal manipulation | Yes | No
Can perform active debugging (producing fuzzing signals) | Yes | No

## Slide 45: hwdbg is available at: https://github.com/HyperDbg/hwdbg

## Slide 46: Questions
Any questions?

## Slide 47: Thank you!
Do you have any questions?
Mail: sina@hyperdbg.org
Twitter: @Intel80x86
Blog: rayanfam.com
or
https://github.com/orgs/HyperDbg/discussions