## Slide 1: hwdbg Debugging Hardware Like Software
Mohammad Sina Karvandi *, Soroush Meghdadizanjani **, Saleh Khalaj Monfared ***, Erik van der Kouwe *, Asia Slowinska *
* Vrije Universiteit Amsterdam (VUSec), The Netherlands
** Stony Brook University (SBU), United States
*** Worcester Polytechnic Institute (WPI), United States
EuroSec 2025

## Slide 2: “To err is human, to debug is divine.”

## Slide 3
Debugging Hardware like Software
Hardware Debugger
3

## Slide 4: Key (must-have) Software Debugger Features
Reading or Writing Memory
Inspecting or Modifying Registers Values
Putting Breakpoints and Pausing The Debuggee
Stepping Through Instructions
Memory
Breakpoint
Registers
Stepping
4

## Slide 5: Mapping Software Concepts to Hardware Logic Analyzer Emulation of Instruction Stepping by Controlling Clock Signal Signal Inspection and Modification Cutting The Signals Based on Conditions
Reading/Writing Memory
Stepping Through Instructions
Inspecting/Modifying Registers Values
Putting Breakpoints and Pausing The Debuggee
5

## Slide 6: Key Intuition
Allow security researchers and hardware engineers to run custom actions
Run in smallest (shortest) event in digital circuit: rising and falling edge of the clock cycle
6

## Slide 7
hwdbg is a debugger chip generator based on chisel language (scala) & LLVM circt
7

## Slide 8: Key Features Signal Analyzer Signal Manipulator Testing & Fuzzing Software Abstractions
Open-source logic analyzer
Manipulating digital signals by changing the state of wires
Automatic testing and fuzzing chips with software-generated test cases
Simulate software debugging concepts in hardware
Not just a passive debugger, it can actively modify signals
8

## Slide 9: Why do we need hwdbg for security? cut signal fuzzing change clock domain
remove signal at random stages
using PWM with different duty cycles
hardware side channels
reverse engineering
fault injection
9

## Slide 10: What are hardware side channels?
Side-channel attacks in chips and IP cores
- Exploit indirect information leakage (e.g., power consumption, electromagnetic emissions)
- Used to extract sensitive data
Detection using sensors
- Ring Oscillators (RO) are used for monitoring
- Detect variations in hardware characteristics
- Identify potential side-channel leakage or attacks
Hardware side channels often use debugging signals
10

## Slide 11: IDELAYE2/3 Time-to-Digital Converter (TDC) Debugging Sensors Ring Oscillator (RO)
Provides adjustable signal delay capabilities for timing adjustments and alignment in high-speed circuits
Converts time interval between two events into digital value for precise timing measurements
Measures variations in signal propagation delay to detect changes in environmental conditions or circuit behavior
11

## Slide 12: Frequency & Clock Sensors Temperature Sensor Debugging Sensors (cont.) Voltage Sensor
Monitors frequency and stability of clock signals to ensure they remain within expected range and performance criteria
Measures temperature within chip to monitor thermal conditions and prevent overheating
Monitors and measures voltage levels within circuit to ensure stable and correct operation
12

## Slide 13: hwdbg is available at: https://url.hyperdbg.org/hwdbg-repo Documentation: https://hwdbg.hyperdbg.org/docs
13

## Slide 14: Backup!
Backup slides…
14

## Slide 15: What is HyperDbg?
HyperDbg is an open-source platform that brings debugging infrastructures like hypervisor-assisted, user-mode, and kernel-mode debuggers mainly with a focus on using modern hardware technologies for analyzing, fuzzing, and reversing.

## Slide 16: Key Contributions
hwdbg comes with these contributions.
Introduction of a Unified Debugging Framework
Open-source and Customizable Tool
Integration with FPGAs
Robust Debugging Experience
Enhancement of Reverse Engineering and Chip Fuzzing Capabilities
Comprehensive Scripting Support
16

## Slide 17: Hardware Platform Software 01 02 03
The hardware side will be written in chisel programming language as well as Verilog and SystemVerilog.
The testing platform is AMD Xilinx FPGAs.
The software side is implemented in C/C++ for sending debugging commands and parsing scripts.
17

## Slide 18
Script Execution Stages
This picture demonstrates the execution of different IR scripts in each stage.
18

## Slide 19: Passive debugging Active debugging Debugging Modes
In this debugging mode, hwdbg acts as an introspection tool, and monitors different signals to the target debugging module.
In this debugging mode, hwdbg is able to both monitor and manipulate signals (Input/Output). These signal modifications are configured by the user’s custom scripts.
19

## Slide 20: Communication Modules —Sending Module —Send/Receive Synchronization Module —Receiving Module —Interpreting Module
Sending module is responsible for preparing mandatory headers and write to BRAM as well as interrupting PS.
Because only one BRAM port is shared with PL, synchronization is needed to avoid data corruption in case of simultaneous writes.
Once share PS <> PL line is high, receiving verifies BRAM data headers and notifies interpreter.
Once a valid packet is received, the interpreting module configures the chips and sends the response to the debugger.
20

## Slide 21: Physical Unclonable Function (PUF)
These unique differences, such as variations in silicon pathways, ensure that each PUF is unique and make it theoretically impossible to duplicate or clone.
A PUF is a physical entity utilized in microchips and other electronic devices to generate unique, device-specific cryptographic keys based on the uncontrollable physical variations that occur during the manufacturing process.
What is PUF?
What is special about PUFs?
21

## Slide 22: BRAM Simulator
Here is the BRAM simulator (PS to PL area).
22

## Slide 23: BRAM Simulator (cont.)
Here is the BRAM simulator (PL to PS area).
23

## Slide 24: BRAM Simulator Waves
Here is the BRAM simulator wave results for hwdbg.
24

## Slide 25: Anomalies In Expected Functionalities Anomalies Based On Sensors Indications Anomaly Definition
These occur when the device fails to compute the correct output due to specific inputs, detectable through emulation.
Sensors can indicate anomalies through abnormal state changes, signaling potential internal issues in the chip.
25

## Slide 26: Supported Operators
Precedence | Operators
Parentheses | ( )
Unary Operators | -, +, ~, &, *
Arithmetic Operators | *, /, %
Arithmetic Operators | +, -
Shift Operators | >>, <<
Comparison Operators | >=, <=, >, ==, !=
Bitwise AND Operator | &
Bitwise XOR Operator | ^
Logical AND Operator | &&
Logical OR Operator | ¦¦
26

## Slide 27: dslang vs TSM
 | hwdbg (dslang) | Xilinx ILA (TSM)
Can act as a logic analyzer | Yes | Yes
Speed comparison | Slower | Faster
Can trigger an event (e.g., a breakpoint) | Yes | Yes
Has debugging sensors | Yes | No
Can modify signals on the fly (configurable) | Yes | No
Can interpret complex computations | Yes | No
Supports on-the-fly configuration | Yes | No
Notify the debugger without triggering event | Yes | No
Supports software stepping | Yes | No
Simplicity of state machine scripting | Simpler, software-like scripting | More complex
Can perform stepping fault-injection and signal manipulation | Yes | No
Can perform active debugging (producing fuzzing signals) | Yes | No
27

## Slide 28: Example Script 1
? {
if (@hw_port5 == 55) {
printf(“@hw_port5 is equal to 0x55\n");
}
elsif(@hw_port5 == 66) {
printf(“@hw_port5 is equal to 0x66\n");
}
elsif(@hw_port5 == 77) {
printf(“@hw_port5 is equal to 0x77\n");
} else {
printf(“@hw_port5 is not equal to 0x55, 0x66, 0x77. It is equal to %llx\n", @hw_port5);
}
}
28

## Slide 29: Example Script 2
? {
int my_func1(int var1) {
result = var1 + 1;
printf("my_func1 %d\n", result);
return result;
}
int my_func2(int var1) {
result = var1 * 2;
printf("my_func2 %d\n", result);
return result;
}
int my_func3(int var1) {
result = my_func1(var1) + my_func2(var1);
printf("my_func3 %d\n", result);
return result;
}
printf("%d\n", my_func3(2));
}
29

## Slide 30: Software Stepping in Hardware
- Once we can control the clock signal, we are able to see and modify I/O ports at each cycle.
- The next rising-edge clock will be inserted once the introspection/modification is done.
- Not possible in chips with internal clock sources.
30

## Slide 31: Thanks!
Do you have any questions?
m.s.karvandi@vu.nl
vusec.net
Please keep this slide for attribution